## Slide 1
A MODEL SOLID WASTE MANAGEMENT SYSTEM AT COMMUNITY LEVEL
GROUP 4
|| PAGE 1
CE 404
Capstone Project
Presented By
1904070 Humaira Jannat Taki (DTL)
1904072 Shahriare Mahmud Sakib (TL)
1904075 Muaz Hossain Mahi
1904076 Fahim Zafri
1904080 Md. Ausaf Alam
1904082 Akash Saha

## Slide 2: Background and Vision of the project
Rapid population growth in Dhaka has overwhelmed the current solid waste management system.
Existing infrastructure is unsustainable, causing pollution, land wastage, and inconvenience to city life.
A redeveloped Secondary Waste Transfer Station will enable:
Doorstep segregated waste collection
  Efficient waste compaction, segregation, and recycling
  Better waste transport systems
  Reduction in environmental pollution and resource wastage
Problem of Statement :
|| PAGE 2

## Slide 3: Project Description & Location
Figure: Google Map: (a) Polashi Waste Transfer Station; (b)Disposal land, Matuali; (c) Effect of Present Solid Waste Management at Matuail
(b)
(c)
Project Background
Project Location
(a)
|| PAGE 3
Dhakeshwari Road,
Ward No. 26
Dhaka South City Corporation.
Latitude 23° 72' 42" and Longitude 90° 38' 86"

## Slide 4
Sponsoring Ministry
Implementing Agency
Project Objective
Estimated Project Budget
Sector & Sub-Sector
Project Category
Geographic Location
Project Duration
Ministry of Local Government
Dhaka South City Corporation (DSCC)
Implement a Sustainable Solid Waste Management System
4.10 Crore (BDT)
Environment
Yellow
Dhaka South City Corporation, Lalbag, Dhaka, Bangladesh
1 Years
Basic Information
|| PAGE 4

## Slide 5: Feasibility Analysis
Field Visit and Conditional Survey
|| PAGE 5
A. Existing Condition
B. Containers
Number-7
Volume- 5 tons
Dimension- 10’x5.5’x6’
C. Vans
Number-30
Volume- 1500 kg
Dimension- 2m x1m x 2m
Collection points: Chawkbazar,
Lalbagh, Azimpur Colony
2 trips per day per van
D. Trucks
Number-2 (One container at a time)
Time: 11:30 PM- 12:00 AM
Transferred to Jatrabari

## Slide 6: Feasibility Analysis
Case Study
|| PAGE 6
 | Star Square Ultra-Modern Mechanized Garbage Transfer Station at Indore, India | Jinxiang Wet Garbage Station at Changsha, China | Waste Compaction Station at the city of Kolkata, India | Secondary Waste Transfer Station at Lalbagh, Dhaka
Waste Collection Process | Separate (Dry-Wet) | Separate (Dry-Wet) | Separate (Dry-Wet) | Mixed
Waste Segregation System | Both manual and Automatic | Automatic | Manual | Absent
Waste Recycling Process | Moderate | Full | Partial | No Recycle
Compactor | Auto Pilot mode | Full automatic computerized | Manual mode | Absent

## Slide 7
Feasibility Analysis
Table: Traffic Flow situation
a
b
c
Figure: Collection routes: (a) Azimpur Colony; (b) Chawkbazar; (c) Lalbagh
Capacity
  2424 PCU/hour
Demand
  2041 PCU/hour
Traffic Impact Analysis
|| PAGE 7

## Slide 8
Feasibility Analysis
|| PAGE 8

## Slide 9
Feasibility Analysis
A
B
C
D
Pre- Construction
Community awareness
Traffic & Access Planning
A
During Construction
Noise Pollution Check
Air Pollution Check
Water quality Check
Soil Pollution Check
Worker health and safety
B
C
D
Environmental Mitigation Measures
Environmental Management Plan
Air, Noise, Soil, Water Quality Check
EHS Officer Appoint
Cost of Monitoring : 48,94,000 BDT
Post Construction
Segregated waste collection system
Adequate drainage for leachate
Recycling of dry waste
|| PAGE 9

## Slide 10
Feasibility Analysis
|| PAGE 10
Preliminary Cost Estimate | 
Soil Investigation Cost | : 1.84 Lac BDT
Foundation Cost | : 37.43 Lac BDT
Super-structure Cost | : 109.32 Lac BDT
Additional Super-structure Cost | : 71.95 Lac BDT
Other Building Cost | : 27.52 Lac BDT
Equipment Cost | : 72.25 Lac BDT
Grand Total Construction Cost | : 463.03 Lac BDT

## Slide 11
Feasibility Analysis
TOTAL COST
1 lac 84 thousands BDT
PRE-CONSTRUCTION
PHASE
4 crore 12 Lac 40 Thousands BDT
CONSTRUCTION PHASE
48 lac 50 thousands BDT
POST CONSTRUCTION
PHASE
Soil Investigation
Environmental Monitoring
Materials, Labor
& Equipment
Operation &
Maintenance
Legal & Administrative Cost
Quality Assurance Cost
60 lac BDT
3 lac BDT
12 lac 45 thousands BDT
SOURCE | RATE | TOTAL REVENUE PER YEAR
Reuse/ Recycle | TK. 25,000 per ton | 350 Lacs
Waste Collection Bill | TK. 60,000 per month | 7 Lacs 20 Thousands
REVENUE BREAKDOWN
|| PAGE 11
Cost Benefit Analysis

## Slide 12
Feasibility Analysis
NPV
IRR
DISCOUNT RATE
BENEFIT-COST RATIO
4 Crore 87 Lac BDT
0.2%
12%
0.73
|| PAGE 12
Cost Benefit Analysis

## Slide 13
Wind Load Provision
Basic Wind Speed: 65.7 m/s
Occupancy Category: III
Exposure Category: A
Importance Factor: 1.15
Seismic Zone: 2 (z=0.2)
Occupancy Category: III
Site Class: SC Seismic Design Category: SDC C
Importance Factor: 1.15
Earthquake Load Provision
Basis of Design (BOD)
Design life : 20 years
Design Standard: BNBC 2020, ACI 318-08, AISC 14
Fire design Standard: ASCE 29, BNBC 2020, Part IV, Chapter 1
Others
Gravity load :
BNBC 2020, Part VI, Chapter 2
Wall construction:
190mm hollow concrete blocks with a density of 1,280kg/m³ and a strength grade of MU15
Damp proof course:
A 60mm C15 fine aggregate concrete layer is
Doors & Windows:
Wooden door and sliding glass windows
|| PAGE 13

## Slide 14
2. Transfer Station:
Dimensions: 17.07 x 14.96 m
Floor Area: 255.36 m²
Height: 9.144 m
Building Area:
Total Area: 300 m²
Base Area: 368 m²
1. Office Building :
Dimensions: 5.48 x 4.87 m and 5.48 x 3.2 m
Floor Area:
26.68 m² and 17.53 m²
Height: 3.048 m
Structural Style:
Foundation: Shallow and Square Foundation
Main Body: RCC Frame Structure
Building Dimension
Building Construction
1. Wall Body: Brick Masonry
Roof:
Office: RCC Roof
Station: Steel Truss Roof
2. Floor: Cement mortar floor,
tile floor
3.Windows & Doors:
Glass Window, Wooden Door
for office
Plastic door for bathroom
Steel Shutter for station building
Basis of Design (BOD)
|| PAGE 14

## Slide 15
|| PAGE 15
ARCHITECTURAL DRAWING WITH ALTERNATIVES
(1)
(2)
(3)

## Slide 16
TECHNICAL AND ENGINEERING ANALYSIS
|| PAGE 16
1.4D
1.2D + 1.6L
1.2D + (Lor 0.8W)
4. 1.2D+ 1.6W + L
5. 1.2D+ E+ L
6. 0.9D+ 1.6W
7. 0.9D+ E
Design Load Combination

## Slide 17
TECHNICAL AND ENGINEERING ANALYSIS
|| PAGE 17
Finalized Design Sections

## Slide 18
1904080
Details Drawing
Building Dimensions:
16,800 x 14,700 mm
Key Sections:
Office Room 1: 2600 x 4600 mm
Office Room 2: 3000 x 3000 mm
Staff Room: 3300 x 3150 mm
Additional Features:
Van Parking: 1050 x 1300 mm
Ground Floor Plan
Fig: Ground Floor plan
|| PAGE 18

## Slide 19
Grade Beam Layout
1904080
|| PAGE 19
Details Drawing
Rectangular Beam
12”x 18”
Type of Beam
G1:
Section Near Column:
3-16 Ø Thru, 10 Ø @ 85 mm C/C.
Mid Span Section:
3-16 Ø Thru, 10 Ø @ 175 mm C/C.
G2:
Section Near Column:
3-16 Ø Thru, 10 Ø @ 85 mm C/C, 2-16 Ø Ext.
Mid Span Section:
3-16 Ø Thru, 10 Ø @ 175 mm C/C.
Fig: Grade beam layout

## Slide 20
Square Column
Reinforced with Longitudinal bars and lateral ties
Type of column
1904080
|| PAGE 20
Office Col : 12”x12” , 10’ height
STS Col : 16”x16”, 20’ height
3 Types of Detailing: C1, C2, C3
Column Dimension
C1: 100 mm | S: 200 mm | lo: 450 mm | L: 3000 mm
C2:125 mm | S: 250 mm | lo: 925 mm | L: 6000 mm
C3:125 mm | S: 250 mm | lo: 925 mm | L: 6000 mm
Details Drawing
Column Design Overview
Fig: Column Layout

## Slide 21
vRectangular Beam
Beam Design overview
1904080
|| PAGE 21
Beam Layout:
Section Details:
Section X-X:
  3-16 Ø Thru, 10 Ø @ 85 mm C/C.
Section Y-Y:
  3-16 Ø Thru, 10 Ø @ 175 mm C/C.
Stirrups Legend:
A: 10 Ø @ 85 mm C/C
B: 10 Ø @ 175 mm C/C
C: 10 Ø @ 100 mm C/C
Details Drawing
Fig: Beam Detailing

## Slide 22
Details Drawing
Office room
|| PAGE 22
Edge Supported Two way slab
Discontinuous at four edges
Type of Slab
(A): Ø10 mm bar @ 225 mm c/c (Straight Bottom)
(B): Ø10 mm bar @ 250 mm c/c (Straight Top)
(C): Ø10 mm corner bar @ 250 mm c/c
Diagonally at top, perpendicular at bottom
(A): Ø10 mm bar @ 250 mm c/c (Straight Bottom)
(B): Ø10 mm bar @ 250 mm c/c (Straight Top)
(C): Ø10 mm corner bar @ 250 mm c/c
Diagonally at top, perpendicular at bottom
Staff room
Fig: Slab layout

## Slide 23
Details Drawing
Square footing
Reinforced with Longitudinal bars and lateral ties
Type of Footing
|| PAGE 23
Footing Layout and Reinforcement Details
Footing Layout:
  Footing Types: F1, F2, F3
  Gridlines: A-D (Vertical) and 1-6 (Horizontal).
  Underground Water Reservoir and Pit marked.
Reinforcement Schedule:
  F1: 1200 x 1200 mm
    Ø12 mm @ 150 mm c/c (Bottom & Top Bars).
  F2: 1350 x 1350 mm
    Ø16 mm @ 200 mm c/c (Bottom & Top Bars).
  F3: 1500 x 1500 mm
    Ø16 mm @ 175 mm c/c (Bottom & Top Bars).
Fig: Footing layout

## Slide 24
Details Drawing
Design consideration
Cover slab – design for horizontal bending (slab action)
Side walls – design for vertical bending (cantilever action) and horizontal bending (slab action)
Base slab – design for horizontal bending (slab action)
Design conditions – 3 Types
When tank is full with water and no soil Outside
When tank is full with water and saturated soil Outside
When tank is empty and saturated soil Outside
Critical Design condition:
Considering last condition as Critical one for design underground water reservoir
Cover and base slab- two way edge supported slab
|| PAGE 24
Fig: Underground water reservoir

## Slide 25
Details Drawing
Reservoir dimensions – 3.6 X 3 X 1.8 m
Reinforcement required at the both sides of side wall
Extended base slab act as anti-uplift shear key
No direct tension steels needed in base slab and Side wall
Design Results
|| PAGE 25
Fig: Underground water reservoir

## Slide 26
Details Drawing
Symmetrical 2D Pratt truss
Joints are connected through bolts and gusset plate
Roof Truss Joint
|| PAGE 26
Truss Dimensions:
Span: 14,940 mm
Height: 3,345 mm
Member Details:
Main Members: L 3x3x1/2
Purlins: C 6x13
Joint Spacing:
Horizontal: 2,490 mm (each segment)
Vertical: 1,115 mm
Key Sections:
Supports at F and central joint A
Diagonal bracing for structural stability
Fig: Roof truss joint
Fig: Truss joint Connections

## Slide 27
Details Drawing
Plumbing Layout Plan
Key Features:
  Water Supply Stack: Ø 37 mm CPVC Pipe
  Wastewater and Soil Stack: Ø 100 mm UPVC Pipe
  Vent Pipe: Ø 50 mm UPVC Pipe
Grid Alignment:
  Vertical: A-D
  Horizontal: 1-6
Main Elements:
  Pit: 1500 x 1500 mm
  Connections to Municipal Sewage Line.
Fig: Plumbing Layout
|| PAGE 27

## Slide 28
Bill Of Quantity(BOQ)
|| PAGE: 28
Chart: 
| Soil Investigation | Earthwork Excavation | Brick Flat Soling | RCC Works | Concrete Reinforcement | Structural Steel | Brick Work | Door Window Glasswork | Plastering | Painting | Formwork(Steel) | Roof Finish | Sanitary and water supply works | Tiles work | False ceiling | Fence | Gate | Safety Net and Scafolding | Testing cost | Additional cost | General, Site facility & Engineering Cost
% of Total Cost | 0.45 | 0.57 | 0.46 | 1.76 | 34.56 | 17.17 | 2.46 | 2.34 | 0.9 | 0.85 | 0.66 | 0.01 | 0.66 | 0.31 | 0.06 | 1.83 | 0.09 | 0.85 | 0.93 | 31.42 | 1.66
Grand Total Cost: 4,09,44,539 BDT
Four Crore Nine Lac Forty Four Thousand
Five Hundred Thirty Nine Taka

## Slide 29
Implementation Timeline
Pre-Construction Phase (Weeks 0-22)
Key Activities:
  Project Initiation: 3 weeks
  Subsoil Investigation: 2 weeks
  Reconnaissance Survey: 3 weeks
  Land & Topographic Surveys: 1-2 weeks
  Environmental Impact Analysis: 4 weeks
  Feasibility Report Preparation: 4 weeks
  Preliminary & Detailed Design: 4 weeks
  BOQ Preparation: 2 weeks
  Tendering: 4 weeks
Construction Phase (Weeks 28-50)
Key Activities:
  Site Preparation: 3 weeks
  Excavation and Earthwork: 6 weeks
  Foundation Work: 6 weeks
  Pit Construction: 2 weeks
  Underground Water Tank: 4 weeks
  Septic Tank: 4 weeks
  Columns, Grade Beams, Lintel, Beams: 20 weeks
  Masonry Works: 2 weeks
  Steel Structure Works: 2 weeks
  Interior Design and Finish: 2 weeks
|| PAGE 29

## Slide 30
|| PAGE 30

## Slide 31
Conclusion
Modernization and Expansion:
  Expansion of the existing STS with modern container trucks and advanced waste compaction techniques
Environmental and Social Benefits:
  Adherence to Environmental Conservation Rules 2023 to minimize impact and improve residents' quality of life.
Economic Viability:
  Despite initial financial challenges, the project demonstrates long-term benefits for the environment, public health, and society.
Innovative Solutions:
  Use of advanced technologies, including compartmentalized tricycles and steel frame structures, setting benchmarks for urban waste management.
|| PAGE 31

## Slide 32: THANK YOU! ANY QUESTIONS?
|| PAGE 32